## Slide 1
Smart Doorbell
A photo of every visitor — instantly
An ESP32-CAM smart doorbell. A visitor presses the button; the device snaps a photo, uploads it to the cloud, and sends a Telegram alert the homeowner answers in one tap.
Includes:
Problem: a normal doorbell can’t show who came or let you reply when you’re away.
What it is: an ESP32-CAM doorbell that sends every visitor’s photo to your phone over Telegram.
Main features: instant photo alert with one-tap reply; live, password-protected dashboard with history, photos and stats; real-time online status from a per-minute heartbeat.
Unique: no app to install — it uses the Telegram you already have, plus optional on-device face recognition.
How it works
Doorbell press
ESP32-CAM wakes and snaps a photo
Secure upload
Photo sent to the cloud over HTTPS
Cloud backend
FastAPI stores the visit, photo and status
Instant alert
Telegram message with one-tap reply
Live dashboard
Visit and reply shown in real time
Wiring diagram
(replace with image)
Dashboard screenshot
(replace with image)
Prototype photo
(replace with image)
ESP32-CAM on the CS-CAM board; button on GPIO13, status LED on GPIO4.
Secure dashboard: visit history, photos, stats and live device status.
The assembled doorbell unit.
Yussef Zarkawi · [team members] — Group 15
Lecturer: [name] · Instructor: [name]
In collaboration with ICST — The Interdisciplinary Center for Smart Technologies, Technion